## Slide 1
AI-Based Real Time Anomaly Detection
& Autonomous Decision Support System
for Deep Space Missions
Purushothaman S | M25DE1033 | M.Tech — Data Engineering | IIT Jodhpur
India Space Academy | AI & Machine Learning in Space Exploration | 2025 – 2026
4
ML Models
8
Docker Services
3
Decision Layers
20K+
Dataset Rows
21
Sensors
1

## Slide 2
AGENDA
2
Presentation Outline
01
Problem
Statement
Why autonomous AI
is needed in space
02
Dataset
NASA C-MAPSS FD001
selection rationale
03
Architecture
Four-layer system
design and data flow
04
ML Models
Anomaly detection
+ RUL prediction
05
Decision
Engine
Rules, risk scoring
and RL agent
06
Deployment
Docker, API, Kafka
Prometheus, Grafana
07
🔴 Live
Stream
Kafka → API →
Dashboard real-time
08
Results &
Advantages
Performance metrics
and project strengths

## Slide 3
PROBLEM STATEMENT
Why Does This System Exist?
The communication delay problem that makes ground control impossible
3
44
MINUTES
Round-trip signal delay to Mars — too late to respond to any emergency
SIGNAL DELAY
ISS
< 0.001 sec
Moon
1.3 sec
Aditya-L1
5 sec
Mars
3–22 min
THE PROBLEM
No Real-Time Control
Any fault response from Earth arrives 44 minutes too late.
Mission-Ending Risk
Critical faults escalate faster than any ground command.
The Solution
Autonomous AI that decides on-board — zero Earth contact.
This project builds the autonomous AI that fills those 44 minutes — detecting faults, predicting failure, and acting independently.

## Slide 4
DATASET
NASA C-MAPSS FD001 Dataset
Why this dataset was selected and what it contains
4
100
Engines
turbofans
21
Sensors
per cycle
20,631
Observations
total rows
128–362
Cycles
per engine
Why This Dataset?
Mirrors spacecraft telemetry
Same gradual multi-sensor degradation as reaction wheels, power converters, thermal systems.
Run-to-failure with ground truth
True RUL known at every cycle — enables precise model training and verifiable evaluation.
21 inter-related sensors
Multivariate complexity matches real spacecraft sensor environments and interactions.
NASA high-fidelity simulation
Physics-based origin and standard benchmark — results compare directly against published work.

## Slide 5
ARCHITECTURE
Four-Layer System Architecture
Data enters at Layer 1 and is progressively enriched toward autonomous decisions
5
End-to-End Data Flow
Raw sensor row
26 values: unit, cycle, 3 settings, 21 sensors
RUL calculated
max_cycle − current_cycle per engine
Feature engineering
Rolling mean + cycle diff for 6 key sensors
StandardScaler
Zero mean, unit variance — equal feature weight
Anomaly detection
Isolation Forest + Autoencoder → flag + score
RUL prediction
Random Forest (snapshot) + LSTM (30-cycle window)
Decision engine
NORMAL / CAUTION / WARNING / CRITICAL
Risk + confidence
0.60×RUL + 0.40×Anomaly → score + HIGH/MED/LOW
Delivery
FastAPI + Kafka + Dashboard + Prometheus
01
DATA LAYER
Load → RUL → Features → Scale
02
INTELLIGENCE LAYER
Isolation Forest + Autoencoder + Random Forest + LSTM
03
DECISION LAYER
Rules → Risk → Confidence → Justification → RL Agent
04
DELIVERY LAYER
FastAPI + Kafka + Streamlit + Prometheus + Grafana

## Slide 6
ML MODELS
Machine Learning Models
Two anomaly detectors and two RUL predictors — different approaches, cross-checking results
6
Isolation Forest
Anomaly Detection
Autoencoder NN
Anomaly Detection
Random Forest
RUL Prediction
LSTM
RUL Prediction
Algorithm
Isolation Forest
Dense Autoencoder
Random Forest Ensemble
LSTM + Dropout
Framework
scikit-learn
TensorFlow / Keras
scikit-learn
TensorFlow / Keras
Input
Feature snapshot
Feature snapshot
Feature snapshot
30-cycle sequence
Training data
All engine data
Healthy only RUL>50
80% split
80% sequences
Key param
100 estimators, 5% contam
32→16→8→16→32 bottleneck
100 trees, n_jobs=-1
LSTM(64), 30 epochs
Output
anomaly_flag + score
reconstruction_error
predicted_RUL (cycles)
predicted_RUL (cycles)
Advantage
Fast, no labels needed
Catches multi-sensor patterns
Reliable baseline, fast
Captures degradation trend

## Slide 7
DECISION ENGINE
Autonomous Decision System
Three layers from rule-based logic to self-improving reinforcement learning
7
INPUTS · anomaly_flag + anomaly_score + predicted_RUL → Feed into all three decision layers simultaneously
LAYER 1 — RULE ENGINE
IF Anomaly + RUL ≤ 5
→ CRITICAL: Immediate maintenance
IF Anomaly + RUL ≤ 15
→ HIGH RISK: Urgent inspection
IF Strong anomaly signal
→ WARNING: Strong anomaly
IF Mild anomaly detected
→ WARNING: Monitor closely
IF No anomaly + RUL ≤ 10
→ CAUTION: Nearing failure
IF All clear
→ NORMAL: Operating nominally
LAYER 2 — RISK + CONFIDENCE
Risk Score Formula
Risk = 0.60 × RUL_risk + 0.40 × Anomaly_strength
Range: 0.0 (safe) → 1.0 (imminent failure)
Confidence Level
HIGH
Both signals agree
MEDIUM
One signal is clear
LOW
Signals contradict each other
Plain-English Justification:
"anomaly detected (score=-0.18); RUL critically low (4 cycles)."
LAYER 3 — RL AGENT
Q-Learning Agent
Self-improving through
simulated experience
States
8
anomaly × RUL band
Actions
4
do nothing → shutdown
Top reward
+10
correct emergency shutdown
Worst penalty
−10
no action at critical RUL

## Slide 8
DEPLOYMENT
Deployment Stack — 1 Command, 8 Services
docker compose up --build → everything starts automatically in the correct order
8
Startup Order
1
Pipeline
Trains all ML models, writes outputs/ and models/
2
FastAPI
Loads models, starts inference server on port 8000
3
Streamlit
Waits for pipeline, then starts dashboard on port 8501
4
Kafka Stack
Zookeeper + Kafka broker + consumer start streaming
5
Monitoring
Prometheus scrapes API metrics, Grafana provisions dashboards
Service Reference
Service
Port
URL / Credential
Streamlit Dashboard
8501
http://localhost:8501
FastAPI Docs
8000
http://localhost:8000/docs
FastAPI Predict
8000
http://localhost:8000/predict
Grafana
3000
http://localhost:3000 (admin/admin)
Prometheus
9090
http://localhost:9090
Kafka Broker
9092
localhost:9092
Zookeeper
2181
localhost:2181
Kafka Consumer
—
Internal — streams CSV → API

## Slide 9
DASHBOARD
Streamlit Mission Control Dashboard
Six pages — five static analysis pages + one real-time live stream page
9
http://localhost:8501 · Pages 1–5 read from telemetry_results.csv · Page 6 polls GET /live every 3 seconds — reflects Kafka streaming live
01
Overview & Anomaly Detection
Fleet health at a glance
Fleet KPI cards: total records, anomalies, critical cases
Health gauges: alert level, health %, failure risk, risk score
Animated status badge: NOMINAL / WARNING / CRITICAL
Anomaly score timeline with color-coded normal vs anomaly points
Recommended action distribution chart and telemetry data table
02
RUL Prediction & Model Compare
Baseline vs deep learning
Actual vs predicted RUL line chart for selected engine
Absolute prediction error area chart over time
RF vs LSTM metrics side-by-side: MAE, RMSE, R²
Scatter plot of all predictions across all 100 engines
03
Risk Score & Decision Confidence
Quantified risk with explanation
Risk gauge dial showing current risk (0–100%)
Confidence level indicator: HIGH / MEDIUM / LOW
Decision justification card — plain-English reasoning
Risk score timeline with 0.4 warning and 0.7 critical lines
04
Autoencoder Analysis
Deep learning anomaly insights
Reconstruction error chart over full engine life
Isolation Forest vs Autoencoder comparison pie charts
Model agreement bar chart: both detect, IF only, AE only
Autoencoder evaluation classification report
05
Reinforcement Learning Demo
Interactive policy learning
Interactive Q-table trainer with 4 sliders
Train agent on demand: episodes, α, γ, ε
Learned policy table: best action per state
Q-value heatmap coloured green (good) to red (bad)
06
🔴 Live Stream
Real-time Kafka → API → Dashboard
Polls GET /live every 2/3/5/10 seconds (user choice)
Status bar: latest unit, cycle, RUL, risk, action, latency
5 KPI cards: total predictions, anomalies, normal, avg RUL, avg risk
Anomaly score scatter chart — green normal / red anomaly dots

## Slide 10
LIVE STREAM
🔴 Live Stream — Real-Time Dashboard Integration
Every Kafka → API prediction reflects on the dashboard within seconds via GET /live polling
10
1
Kafka Producer
Reads telemetry_results.csv
Publishes to topic:
telemetry-input
0.3 sec between rows
2
Kafka Consumer
Subscribes to topic
Receives each row
Forwards to POST /predict
3
FastAPI /predict
Runs AI models
Decision engine
Appends to
LIVE_PREDICTIONS deque
4
GET /live
Returns last 200
predictions as JSON
Polled every 3s by
Streamlit page
5
Live Stream Page
Re-renders charts
Status bar: green/amber/red
KPI cards + table
update in real time
What Renders on Each Poll Cycle
Status Bar
Latest unit, cycle, RUL, risk, action, latency — green/amber/red
5 KPI Cards
Total predictions, anomalies, normal, avg RUL, avg risk
Anomaly Score Scatter
Green dots = normal | Red dots = anomaly
Predicted RUL Line
RUL estimate evolving as predictions arrive
Risk Score Area Chart
Running risk with 0.4 warning + 0.7 critical lines
Live Feed Table
Last 20 predictions newest-first with timestamps

## Slide 11
MONITORING
Grafana Monitoring Setup
9 panels to monitor API health, latency, anomaly rates, and system resources
11
Setup Steps (run once after docker compose up --build)
1. Open http://localhost:3000 → Login: admin / admin
2. Settings → Data Sources → Add → Prometheus
3. URL field: http://prometheus:9090 → Save and Test → green tick
4. Dashboards → New → New Dashboard → Add Visualization
5. Add each panel using the PromQL queries listed on the right
6. Arrange panels into 3 rows → Name dashboard → Save
7. Set auto-refresh to 5s using the dropdown at top-right
Key PromQL Queries (paste into query editor)
Total Requests
telemetry_prediction_requests_total
Failure Rate %
100 * failures_total / requests_total
Anomaly Rate %
100 * anomalies_total / requests_total
Avg Latency
rate(latency_sum[5m]) / rate(latency_count[5m])
P95 Latency
histogram_quantile(0.95, rate(latency_bucket[5m]))
Memory (RSS)
process_resident_memory_bytes
CPU Rate
rate(process_cpu_seconds_total[5m])
Memory Leak Check
python_gc_objects_uncollectable_total
Anomalies Over Time
rate(telemetry_anomalies_detected_total[5m])

## Slide 12
RESULTS
Results & Key Advantages
Live performance metrics and what makes this project stand out
12
~0.38s
Avg API latency
326
Predictions processed
0
Prediction failures
2.76%
Anomaly rate (live)
Fully Autonomous
Zero human input from sensor to recommendation. Works during 44-min Mars blackout.
Multi-Model Redundancy
Two anomaly detectors + two RUL predictors cross-check each other. No single point of failure.
Explainable AI
Every decision has a plain-English justification. Fully auditable for aerospace certification.
Self-Improving via RL
Q-learning agent discovers optimal policies for situations not explicitly programmed.
Production-Grade Deploy
8 Docker containers, single command, runs on any machine — laptop or spacecraft.
Live Self-Monitoring
Prometheus + Grafana track every request, latency, anomaly — system monitors itself.

## Slide 13
KEY TAKEAWAYS
Real aerospace problem solved
44-minute Mars delay makes ground control impossible. This system fills that gap.
Complete end-to-end system
Raw sensor data → AI models → live dashboard, API, Kafka, monitoring — one command.
Live streaming dashboard
Every Kafka prediction reflects on the dashboard in real time via GET /live polling.
Transparent and trustworthy AI
Explainable decisions, self-monitoring, no black boxes — aerospace-grade.
This system demonstrates that
autonomous AI health management
for deep space missions is
achievable today.
Purushothaman S
M25DE1033 | M.Tech Data Engineering | IIT Jodhpur
Technology Stack:
Python | TensorFlow | scikit-learn | FastAPI | Kafka | Streamlit | Docker | Prometheus | Grafana
Thank You
13